## Slide 1: Introduction to Geographical Information Systems (GIS)
Engineer Salahuddin Jokhio, E.B, E.M
Lecturer, CSE, IICT
MUET Jamshoro, Sindh, Pakistan
LECTURE # 04

## Slide 2: Vector data modeling
This lecture is on

## Slide 3: Vector Data Models
Vector Data uses Points and their (X,Y) coordinates to represent spatial features
Precisely position features in space
  Points, Nodes, vertex, single X,Y coordinate pair
  Lines, Arcs, series of X,Y coordinate pairs
  Area, Polygons, area as a closed loop of X,Y coordinate pairs

## Slide 4: Vectors and Data? How?
Here it is…

## Slide 6: Points
A point is a 0 dimensional object and has only the property of location (x,y).
Points can be used to Model features such as a well, building, power, pole, sample location etc.
Other name for a point are vertex, node, 0-cell.

## Slide 7: Lines
A line is a one-dimensional object that has the property of length.
Lines can be used to represent road, streams, faults, dikes, maker beds, boundary, contacts etc.
Lines are also called an edge, link, chain, arc, 1-cell.
In an ArcInfo coverage an arc starts with a node, has zero or more vertices, and ends with a node.

## Slide 8: Polygons
A polygon is a two-dimensional object with properties of area and perimeter.
A polygon can represent a city, geologic formation, dike, lake, river, etc.
Other name for polygons face, zone 2-cell.
Scale matters... A lot…

## Slide 9: Vector Data Model

## Slide 10: Vector Data Model (review)
Vector storage implies the use of vectors (directional lines) to represent a geographic feature.
Vector data is characterized by the use of sequential points or vertices to define a linear segment. Each vertex consists of an X coordinate and a Y coordinate.
Vector lines are often referred to as arcs and consist of a string of vertices terminated by a node.
  A node is defined as a vertex that starts or ends an arc segment.
Point features are defined by one coordinate pair, a vertex.
Polygonal features are defined by a set of closed coordinate pairs.