## Slide 1: Introduction to Geographical Information Systems (GIS)
Engineer Salahuddin Jokhio, E.B, E.M
Lecturer, CSE, IICT
MUET Jamshoro, Sindh, Pakistan
LECTURE # 05

## Slide 2: Raster data modeling
This lecture is on

## Slide 3: Raster Data Model (Definitions)
Based on pixels (rather than on geometric shapes). (**Can be converted into tables, as we were doing with vector).
Raster Data Model
  A format for storing, processing, and displaying graphic data in which graphic images are stored as values for uniform grid cells or pixels.
Raster data models incorporate the use of a grid-cell data structure where the geographic area is divided into cells identified by row and column. This data structure is commonly called raster.

## Slide 4: Raster Data Model (Definitions)
Pixels
  Abbreviation for picture element, the smallest indivisible element that makes up an image. In raster processing, data is represented spatially on a matrix of grid cells, called pixels, which are assigned values for image characteristics or attributes.
Resolution
  A measure of the accuracy or detail of a graphic display, expressed as dots per inch, pixels per line, lines per millimeter, etc.
Spatial Resolution
  The accuracy associated with the capture of ground information as reproduced in a digital format or graphic display. For example, 10-foot pixels vs. 100-foot pixels.

## Slide 6: Raster (Concepts)
A Raster data model uses a grid of x by y or m by n columns.
Rows and Columns of Cells (Array)
Area of all cells equals Spatial Resolution
Value for each cell records type of object or condition
Cells do not correspond to spatial entities in real world
  A road is a group of cells, not a single entity
Cells are considered Homogeneous Units
One grid cell is one unit or holds one attribute.

## Slide 7: Raster (Concepts)
Every cell has a value, even if it is “missing.”
A cell can hold a number or an index value standing for an attribute.
A cell has a resolution, given as the cell size in ground units.
The raster structure is also called regularly spaced matrix . This data structure involves a division of spatial data into regularly spaced cells.
Each cell is of the same shape and size. Squares are most commonly utilized.

## Slide 8: Generic structure for a grid
Figure 3.1
Generic structure for a grid.
R
o
w
s
Columns
Grid
cell
Grid extent
Resolution

## Slide 9: Raster Data Model
As well, since most data is captured in a vector format, e.g. digitizing, data must be converted to the raster data structure. This is called vector-raster conversion. Most GIS software allows the user to define the raster grid (cell) size for vector-raster conversion. It is imperative that the original scale, e.g. accuracy, of the data be known prior to conversion. The accuracy of the data, often referred to as the resolution, should determine the cell size of the output raster map during conversion.

## Slide 10: Source of Raster Data
Satellite data
Scanned aerial photography
Digital Ortho-photography
Scanned maps and documents
SCANNED Aerial photographs
  photographs are NOT raster images but SCANNED images ARE
SCANNED maps
Satellite images

## Slide 11: Raster Data

## Slide 12: The Mixed Features Problem

## Slide 13: Raster Data