## Slide 1: Introduction to Geographical Information Systems (GIS)
Engineer Salahuddin Jokhio, E.B, E.M
Lecturer, CSE, IICT
MUET Jamshoro, Sindh, Pakistan
LECTURE # 06

## Slide 2: Vector & Raster data model pros n cons & relationship
This lecture is on

## Slide 3: VECTOR DM ADVANTAGES
Data can be represented at its original resolution and form without generalization.
Graphic output is usually more aesthetically pleasing (traditional cartographic representation);
Since most data, e.g. hard copy maps, is in vector form no data conversion is required.
Accurate geographic location of data is maintained.
Allows for efficient encoding of topology, and as a result more efficient operations that require topological information, e.g. proximity, network analysis.

## Slide 4: VECTOR DM DISADVANTAGES
The location of each vertex needs to be stored explicitly.
For effective analysis, vector data must be converted into a topological structure. This is often processing intensive and usually requires extensive data cleaning. As well, topology is static, and any updating or editing of the vector data requires re-building of the topology.
Spatial analysis and filtering within polygons is impossible

## Slide 5
Algorithms for manipulative and analysis functions are complex and may be processing intensive. Often, this inherently limits the functionality for large data sets, e.g. a large number of features.
Continuous data, such as elevation data, is not effectively represented in vector form. Usually substantial data generalization or interpolation is required for these data layers.
VECTOR DM DISADVANTAGES

## Slide 6
The geographic location of each cell is implied by its position in the cell matrix. Accordingly, other than an origin point, e.g. bottom left corner, no geographic coordinates are stored.
Due to the nature of the data storage technique data analysis is usually easy to program and quick to perform.
The inherent nature of raster maps, e.g. one attribute maps, is ideally suited for mathematical modeling and quantitative analysis.
RASTER DM ADVANTAGES

## Slide 7: RASTER DM ADVANTAGES
Discrete data, e.g. forestry stands, is accommodated equally well as continuous data, e.g. elevation data, and facilitates the integrating of the two data types.
Grid-cell systems are very compatible with raster-based output devices, e.g. electrostatic plotters, graphic terminals.

## Slide 8: RASTER DM DISADVANTAGES
The cell size determines the resolution at which the data is represented.;
It is especially difficult to adequately represent linear features depending on the cell resolution. Accordingly, network linkages are difficult to establish.
Most output maps from grid-cell systems do not conform to high-quality cartographic needs.

## Slide 9: RASTER DM DISADVANTAGES
Processing of associated attribute data may be cumbersome if large amounts of data exists. Raster maps inherently reflect only one attribute or characteristic for an area.
Since most input data is in vector form, data must undergo vector-to-raster conversion. Besides increased processing requirements this may introduce data integrity concerns due to generalization and choice of inappropriate cell size.

## Slide 10
Relationship Between Representation & Analysis
Raster
  less compact data structure
  simple data model
  Easier analysis of spatial variability
  Easier analysis of spatial relationships of environmental data
Vector
  More compact data structure
  More complex data model
  Provides analysis of distribution and location of individual objects
  works well with topological relationships (i.e. land parcels & roads)
  difficult overlay processing